## Slide 1
Offline Python Coding Assistant
Qwen3-1.7B (w4a16) running on the Snapdragon X Elite NPU
Snapdragon AI Lab Build & Present Challenge
Built and tested remotely on Qualcomm Device Cloud (Snapdragon X Elite, SC8380XP, Windows 11)

## Slide 2
Problem: students learn to code without reliable internet
Cloud coding assistants need a connection, an account and often a subscription.
Many students have patchy connectivity, or cannot send their code to a third-party server.
A small model that runs fully on the laptop gives instant, private help for Python basics.
Use case: offline Python coding tutor (write, explain and fix short snippets).

## Slide 3
Why on-device, and why the NPU
Offline
No network after the one-time model download. Works in a classroom or on a train.
Private
Student code and prompts never leave the machine.
Efficient
NPU inference leaves CPU and GPU free and is built for low-power, sustained AI workloads.

## Slide 4
What we built, and the honest two-model journey
Final stack (verified)
Model: Qwen3-1.7B w4a16, official Qualcomm bundle (1.6 GiB)
Runtime: GenieX CLI v0.7.0 (QAIRT 2.45)
Device: Qualcomm Device Cloud, CRD8380X (SC8380XP)
Load line: runtime=qairt compute=npu
How we got here
First attempt: Qwen2.5-Coder-1.5B exported to ONNX. It failed at NPU profiling, because the NPU path needs w4a16 quantization.
Switch: Qualcomm's prebuilt Qwen3-1.7B w4a16, which loads and runs on the NPU.

## Slide 5
Measured on the NPU (real runs)
~40-42
tokens/s decode
(range 39-45)
~0.05 s
time to first token
(0.052-0.058 s)
364-733
tokens/s prompt
processing
Live demo (recorded on the device): reverse a string, binary search in 2 lines, Fibonacci generator. All three answers were correct.
Indicative numbers from single short runs, not a formal benchmark.

## Slide 6
Limitations and next steps
Limitations (be honest)
1.7B general model, not code-specialised.
A decorator prompt gave a WRONG answer in an earlier take.
Numbers come from a few short runs.
Tested on Qualcomm Device Cloud; I do not own a Snapdragon laptop.
Next steps
Try a code-tuned model once a w4a16 NPU bundle exists.
Run a proper benchmark set (correctness and latency).
Wrap GenieX in a simple local chat UI for students.
Package an offline installer for classrooms.